Calculated value from Task 2.4
85.11E-6

Exercise 2.1

Part 1
Calculated value for average power = 73.5728 uW

(detailed calculation in the notebook)

TODO: Recheck this value

Part 2
Simulated value for average power = 75.43 uW

Percentage Difference = 2.46215 %

TODO: write reasoning for deviation from value, mention any omission and assumptions in your calculations

Exercise 3.1

With the transistor Wp=1um and Wn=1um (waveform 1) the 1→0 transition is slower than Wp=1um and Wn=10um (waveform 2), which is because the Pull-Down network which comprises of the NMOS transistor has a much larger width in comparison to the PMOS transistor. At the 50% mark, the first waveform is later than the second waveform by 52.47 ps.

In the 0→1 transition, waveform 1 is faster than waveform 2 because although the widths of the PMOS in both waveforms are identical, the PDN comprising of the NMOS transistor has a much lower width. At the 50% mark, the first waveform is ahead of the second waveform by 107.64 ps as the PDN is not as large as the second waveform making it more agile and susceptible to transition from 0→1.

TODO: Explain this phenomenon in more electrical terms

Exercise 5.1

Part 1
See notebook for the sketch of the widths

TODO: Draw the schematic in cadence and take a screenshot of the circuit with the corresponding widths.

Part 2

Worst case propagation delays for circuits (from the Calculation)

Y-circuit

Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.15525 ns
High-low	Low-high	0.2415ns	N/A

(The delay values were compared from Output signal to the input signal of D input)

Inverter Circuit
Circuit is using minimum sized PMOS and NMOS transistors using 1um/0.35um W/L.

Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.05175 ns
High-low	Low-high	0.12075 ns	N/A

Y-custom Circuit

Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.05175 ns
High-low	Low-high	0.12075 ns	N/A

Part 3
See notebook for the sketch of the capacitance nodes and their corresponding capacitances

TODO: Draw the schematic in cadence and take screenshots for each circuit with corresponding node capacitances

Part 4

Propagation Delay	How Estimated	Min-Sized Inverter	Minimum Sized Y	Custom Sized Y
tpLH_WC (ps)	Simulated	138.92	241.18	99.29
	Calculated (no parasitic caps)	120.75	241.5	120.75
	Calculated (with parasitic caps)	144.9	217.35	108.675
	Percentage difference calculated as: (simulated – calculated)/simulated x 100	4.3046 %	9.88059 %	9.4521 %
tpHL_WC (ps)	Simulated	62.91	176.005	56.57
	Calculated (no parasitic caps)	51.75	155.25	51.75
	Calculated (with parasitic caps)	62.1	144.9	54.3375
	Percentage difference calculated as: (simulated – calculated)/simulated x 100	1.2875 %	17.6727 %	3.9464 %

(in the report, show the workings of the calculated values (found in part 2))

TODO: Recheck the simulation values for minimum sized y for t_HL

Part 5
Low-to-high
A: 0→1
B: 0→1
C: 1→0
D: 1→0

High-to-low
A: 0→0
B: 1→0
C: 0→1
D: 0→1

TODO: explain reasoning

Part 6
(Completed as part of above parts, take screenshots of customized y-circuit and put in report)

Part 7

yield = 0.364

Part 8
Category	Process Corners	tpHL_WC	tpLH_WC
MOS Transistor	Typical Mean (TM)	0.094726 ns	0.2267 ns
	Worst Case Speed (WS)	0.16212 ns	0.2451 ns
	Worst Case Power (WP)	0.2754 ns	0.1726 ns
	Worst Case One (WO)	0.09404 ns	0.22902 ns
	Worst Case Zero (WZ)	0.128193 ns	0.27079 ns