# Exercise 3.1

Part 1
Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.07757 ns
High-low	Low-high	0.0907 ns	N/A

Red is input, and Green is output in the above simulation plot.

Part 2
equivalent circuit at the back of ODS notebook

Part 3

Derivation: In ODS notebook (back)

tpd_LH = 0.69*Rp*CL
tpd_LH = 0.0907 ns
CL = 12 fF
Rp = 10954.1 Ω

Part 4

(Analytic result)

Rp = Rp, min x Wmin/W x L/Lmin

Rp, min = 10954.1 x 1/1 * 0.35/0.35 = 10954.1 Ω = 10.954 kΩ

(After Simulation)

Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.06953 ns
High-low	Low-high	0.15645 ns	N/A

Output is Green, and Input is Red in the above simulations.

Rp = 18894.93 Ω = 18.895 kΩ

Rp, min = 18894.93 Ω = 18.895 kΩ

Part 5

tpd_HL = 0.69 x Rn x CL

Rn = 9368.36 Ω = 9.368 kΩ

Rn, min = 9368.36 * 1/1 * 0.35*0.35 = 9368.36 Ω = 9.368 kΩ

___
Note: Recheck values of width and length for part 2, 3

# Exercise 3.2
Part 1
(See ODS Notebook for derivation values)
PMOS W/L = 3.259/0.35 (mu m)
NMOS W/L = 1.61/0.35 (mu m)

Part 2

Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.08802 ns = 88.02 ps
High-low	Low-high	0.1028 ns = 102.8 ps	N/A