# Exercise 3.1

Part 1
Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.0706 ns
High-low	Low-high	0.0206 ns	N/A

Part 3

(do the derivation)

tpd_LH = 0.69*Rp*CL
Rp = 2985.5 Ω

Part 4

Rp = Rp, min x Wmin/W x L/Lmin

Rp, min = 2985.5 x 2/1 * 0.35/0.35 = 5971 Ω

(After Simulation)

Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.15662 ns
High-low	Low-high	0.06964 ns	N/A

Rp = 8410.63 Ω

Rp, min = 8410.63 Ω

Part 5

tpd_HL = 0.69 x Rn x CL

Rn = 9338.62 Ω

Rn, min = 9338.62 * 1/1 * 0.35*0.35 = 9338.62 Ω

______
Notes: recheck part 4 simulation results

# Exercise 3.2
Part 1
(See ODS Notebook for derivation values)
PMOS W/L = 1.45/0.35 (mu m)
NMOS W/L = 1.61/0.35 (mu m)

Part 2

Input	Output	tpd_LH	tpd_HL
Low-high	High-low	N/A	0.0787 ns = 78.7 ps
High-low	Low-high	0.19807 ns = 198.07 ps	N/A